## Slide 1: Circuit Analysis and Design Academic year 2017/2018 – Semester 1 – tutorial 1
Qammer H. Abbasi, Francesco Fioranelli, Petros Karadimas, Majid Butt {qammer.abbasi, francesco.fioranelli, petros.karadimas, majid.butt}@glasgow.ac.uk
“A good student never steal or cheat”

## Slide 2: EXAMPLE 2.4
Find V1, I1, I2, and I3 in the circuit shown in Figure 2.13.
KCL: Is = I1 + I2 + I3 = V1/R1 + V1/R2 + V1/R3 = V1(1/R1 + 1/R2 + 1/R3)
I1 = V1/R1 = 2 mA, I2 = V1/R2 = 4 mA, I3 = V1/R3 = 6 mA

## Slide 3: EXAMPLE 2.5
Given I1 = 3 A, I3 = 10 A, and I6 = – 8 A, find I2, I4, and I5 in the circuit shown in Figure 2.15.
KCL at node 1: I2 + I3 = I1
I2 = I1 – I3 = 3 A – 10 A = – 7 A
KCL at node 3: I1 + I5 + I6 = 0
I5 = – I1 – I6 = – 3 A – (– 8 A) = 5 A
KCL at node 2: I4 = I2 + I5
I4 = I2 + I5 = – 7 A + 5 A = – 2 A

## Slide 4: EXAMPLE 2.6
Find I1, I2, I3, I4, I5, and I6 in the circuit shown in Figure 2.18.
Ohm’s law: I1 = (Vs2 – Vs1)/R1 = 6 V/3  = 2 A, I2 = (Vs2 – Vs1)/R2 = 6 V/6  = 1 A,
I3 = Vs1/R3 = 4 V/1  = 4 A, I4 = Vs2/R4 = 10 V/5  = 2 A
KCL at node 1: I5 = – I1 – I2 + I3 = – 2 A – 1 A + 4 A = 1 A
KCL at node 2: I6 = I1 + I2 + I4 = 2 A + 1 A + 2 A = 5 A

## Slide 5: EXAMPLE 2.8
Given V1 = 6 V, V5 = 5 V, V6 = 3 V, and V7 = 7 V, find V2, V3, V4, and V8 in the circuit shown in Figure 2.23.
KVL around the mesh in the lower left:
– V6 + V4 + V7 = 0, V4 = V6 – V7 = 3 V – 7 V = – 4 V
KVL around the mesh in the lower right:
– V7 – V5 + V8 = 0,
V8 = V5 + V7 = 5 V + 7 V = 12 V
KVL around the mesh in the upper left:
– V1 + V3 – V4 = 0, V3 = V1 + V4 = 6 V – 4 V = 2 V
KVL around the mesh in the upper right:
– V3 + V2 + V5 = 0
V2 = V3 – V5 = 2 V – 5 V = – 3 V

## Slide 6: EXAMPLE 2.9
Find i, V1, V2, I2, I3, I4, I5 in the circuit shown in Figure 2.25.
KVL around the mesh in the lower left: – Vs + R1i + 2500i = 0 or – 7 + 1000i + 2500i = 0
i = 7/3500 A = 1/500 A = 2 mA, V1 = 2500i = 2500  0.002 V = 5 V
KVL around the outside loop:
– Vs + 2000i + V2 = 0
V2 = Vs – 2000i = 7 – 2000  0.002 = 3 V
Ohm’s law:
I4 = (V1 – V2)/R2 = 2 V/2000  = 1 mA
I5 = V2/R3 = 3 V/1500  = 2 mA
KCL at node 1: I3 = i – I4 = 1 mA
KCL at node 2: I1 = I5 – I4 = 1 mA
KCL at node 3: I2 = I1 + i = 3 mA

## Slide 7: EXAMPLE 2.10
Given I3 = 750 A, find Va, I2, I4, I1, Vs in the circuit shown in Figure 2.31.
Ra = R2 + R3 + R4 = 50 k, Rb = R5 + R6 = 20 k, Rc = R7 + R8 + R9 + R10 = 75 k
Va = RbI3 = 15 V, I2 = Va/Ra = 0.3 mA, I4 = Va/Rc = 0.2 mA, I1 = I2 + I3 + I4 = 1.25 mA
V1 = R1I1 = 5 V, Vs = V1 + Va = 20 V
Figure 2.32 shows simplified circuit.